## Slide 1
Six Sigma and Statistical Quality Control

## Slide 2: Outline
Quality and Six Sigma: Basic ideas and history
Juran Trilogy
  Control
  Improvement
  Planning
Quality Strategy
Focus on Statistical Methods
  Process Capability ideas and metrics
  Control charts for attributes and variables

## Slide 3: A Brief History
The Craft System
Taylorism (Scientific Management)
Statistical Quality Control
  Pearson, Shewhart, Dodge
Human Relations School
  Mayo, Maslow, Simon, Herzberg, Likert
The Japanese Revolution (1950)
  Ishikawa, Taguchi, Deming, Juran, Feigenbaum
The USA Wakes Up (1980)
  Crosby
1990s: Six Sigma
The Need for Organizational Change

## Slide 4
JIT and TQM
Walter Shewhart
1891 - 1967
W. Edwards Deming
1900 - 1993
Joseph M. Juran
1904 - 2008

## Slide 5: What is Quality?
Freedom from Defects
  Quality Costs Less
  Affects Costs
Presence of Features
  Quality Costs More
  Affects Revenue

## Slide 6: Juran Trilogy Planning, Control, Improvement

## Slide 7: Juran Trilogy Planning, Control, Improvement
Chronic Waste
Chronic Waste
Sporadic Spike
Planning
Control
Control
Improvement

## Slide 8: Quality Control
Aimed at preventing unwanted changes
Works best if deployed at the point of production or service delivery (Empowerment)
Tools:
  Established, measurable standards
  Measurement and feedback
  Control charts
  Statistical inference

## Slide 9: Quality Control
Operate
Establish Standard
Corrective Action
Measure Performance
Compare to Standard
OK?
Yes
No

## Slide 10: Quality Improvement
Aimed at creating a desirable change
Two distinct “journeys”
  Diagnosis
  Remedy
Project team approach
Tools
  Process flow diagram
  Pareto analysis
  Cause-effect (Ishikawa, fishbone) diagram
  Statistical tools

## Slide 11: Quality Improvement
Identify problem
Analyze symptoms
Formulate theories
Test theories - Identify root cause
Identify remedy
Address cultural resistance
Establish control

## Slide 12: Quality Planning
Aimed at creating or redesigning (re-engineering) a process to satisfy a need
Project team approach
Tools
  Market research
  Failure analysis
  Simulation
  Quality function deployment
  Benchmarking

## Slide 13: Quality Planning
Verify goal
Identify customers
Determine customer needs
Develop product
Develop process
Transfer to operations
Establish control

## Slide 14: Strategic Quality Planning
Mission
Vision
Long-term objectives
Annual goals
Deployment of goals
Assignment of resources
Systematic measurement
Connection to rewards and recognition

## Slide 15: Strategic Quality Planning
Aimed at establishing long-range quality objectives and creating an approach to meeting those objectives
Top management’s job
Integrated with other objectives
  Operations
  Finance
  Marketing
  Human Resources

## Slide 17: Process Capability
The Relationship between a Process and the Requirements of its Customer
How Well Does the Process Meet Customer Needs?

## Slide 18: Process Capability
Specification Limits reflect what the customer needs
Natural Tolerance Limits (a.k.a. Control Limits) reflect what the process is capable of actually delivering
These look similar, but are not the same

## Slide 19: Specification Limits
Determined by the Customer
A Specific Quantitative Definition of “Fitness for Use”
Not Necessarily Related to a Particular Production Process
Not Represented on Control Charts

## Slide 20: Tolerance (Control) Limits
Determined by the inherent central tendency and dispersion of the production process
Represented on Control Charts to help determine whether the process is “under control”
A process under control may not deliver products that meet specifications
A process may deliver acceptable products but still be out of control

## Slide 21: Measures of Process Capability
Cp
Cpk
Percent Defective
Sigma Level

## Slide 22: Example: Cappuccino
Imagine that a franchise food service organization has determined that a critical quality feature of their world-famous cappuccino is the proportion of milk in the beverage, for which they have established specification limits of 54% and 64%.
The corporate headquarters has procured a custom-designed, fully-automated cappuccino machine which has been installed in all the franchise locations.
A sample of one hundred drinks prepared at the company’s Stamford store has a mean milk proportion of 61% and a standard deviation of 3%.

## Slide 23: Example: Cappuccino
Assuming that the process is in control and normally distributed, what proportion of cappuccino drinks at the Stamford store will be nonconforming with respect to milk content?
Try to calculate the Cp, Cpk, and Parts per Million for this process.
If you were the quality manager for this company, what would you say to the store manager and/or to the big boss back at headquarters? What possible actions can be taken at the store level, without changing the inherent variability of this process, to reduce the proportion of non-conforming drinks?

## Slide 24: Lower Control Limit

## Slide 25: Upper Control Limit

## Slide 26: Nonconformance

## Slide 27: Nonconformance

## Slide 28: Nonconformance
0.00990 of the drinks will fall below the lower specification limit.
0.84134 of the drinks will fall below the upper limit.
0.84134 - 0.00990 = 0.83144 of the drinks will conform.
Nonconforming:
  1.0 - 0.83144 = 0.16856 (16.856%)

## Slide 29: Cp Ratio

## Slide 30: Cpk Ratio

## Slide 31: Parts per Million

## Slide 32: Quality Improvement
Two Approaches:
  Center the Process between the Specification Limits
  Reduce Variability

## Slide 33: Approach 1: Center the Process

## Slide 34: Approach 1: Center the Process

## Slide 35: Approach 1: Center the Process

## Slide 36: Approach 1: Center the Process
0.04746 of the drinks will fall below the lower specification limit.
0.95254 of the drinks will fall below the upper limit.
0.95254 - 0.04746 = 0.90508 of the drinks will conform.
Nonconforming:
  1.0 - 0.90508 = 0.09492 (9.492%)

## Slide 37: Approach 1: Center the Process
Nonconformance decreased from 16.9% to 9.5%.
The inherent variability of the process did not change.
Likely to be within operator’s ability.

## Slide 38: Approach 2: Reduce Variability
The only way to reduce nonconformance below 9.5%.
Requires managerial intervention.

## Slide 39: Quality Control
Operate
Establish Standard
Corrective Action
Measure Performance
Compare to Standard
OK?
Yes
No

## Slide 40: Quality Control
Aimed at preventing and detecting unwanted changes
An important consideration is to distinguish between Assignable Variation and Common Variation
Assignable Variation is caused by factors that can clearly be identified and possibly managed
Common Variation is inherent in the production process
We need tools to help tell the difference

## Slide 41: When is Corrective Action Required?
Operator Must Know How They Are Doing
Operator Must Be Able to Compare against the Standard
Operator Must Know What to Do if the Standard Is Not Met

## Slide 42: When is Corrective Action Required?
Use a Chart with the Mean and 3-sigma Limits (Control Limits) Representing the Process Under Control
Train the Operator to Maintain the Chart
Train the Operator to Interpret the Chart

## Slide 43: Example: Run Chart

## Slide 44: When is Corrective Action Required?
Here are four indications that a process is “out of control”. If any one of these things happens, you should stop the machine and call a quality engineer:
One point falls outside the control limits.
Seven points in a row all on one side of the center line.
A run of seven points in a row going up, or a run of seven points in a row going down.
Cycles or other non-random patterns.

## Slide 45: Example: Run Chart

## Slide 46: Type I and Type II Errors

## Slide 47: When is Corrective Action Required?
One point falls outside the control limits.
  0.27% chance of Type I Error
Seven points in a row all on one side of the center line.
  0.78% chance of Type I Error
A run of seven points in a row going up, or a run of seven points in a row going down.
  0.78% chance of Type I Error

## Slide 48: Basic Types of Control Charts
Attributes (“Go – No Go” data)
A simple yes-or-no issue, such as “defective or not”
Data typically are “proportion defective”
p-chart
Variables (Continuous data)
Physical measurements such as dimensions, weight, electrical properties, etc.
Data are typically sample means and standard deviations
X-bar and R chart

## Slide 49: Statistical Symbols (Attributes)

## Slide 50: p-chart Example

## Slide 51: p-chart Example

## Slide 54
Note: If the LCL is negative, we round it up to zero.

## Slide 56: Statistical Symbols (Variables)

## Slide 57: X-bar, R chart Example

## Slide 59
From Exhibit TN7.7

## Slide 63: X-bar Chart

## Slide 64: R chart

## Slide 65: Interpretation
Does any point fall outside the control limits?
Are there seven points in a row all on one side of the center line?
Is there a run of seven points in a row going up, or a run of seven points in a row going down?
Are there cycles or other non-random patterns?

## Slide 66
A Process in which the Specification Limits are Six Standard Deviations above and below the Process Mean
Two Approaches:
Move the Specification Limits Farther Apart
Reduce the Standard Deviation
Six Sigma Defined (Low-Level)

## Slide 67: Approach #1
Ask the Customer to Move the Specification Limits Farther Apart.

## Slide 73: Approach #2
Reduce the Standard Deviation.

## Slide 79: Process Drift
What Happens when the Process Mean Is Not Centered between the Specification Limits?

## Slide 84: Six Sigma: Many Meanings
A Symbol
A Measure
A Benchmark or Goal
A Philosophy
A Method

## Slide 85: Six Sigma: A Symbol
 is a Statistical Symbol for Standard Deviation
Standard Deviation is a Measure of Dispersion, Volatility, or Variability

## Slide 86: Six Sigma: A Measure
The “Sigma Level” of a process can be used to express its capability — how well it performs with respect to customer requirements.
Percent Defects, Cp, Cpk, PPM

## Slide 87: Six Sigma: A Benchmark or Goal
The specific value of 6 Sigma (as opposed to 5 or 4 Sigma) is a benchmark for process excellence.
Adopted by leading organizations as a goal for process capability.

## Slide 88: Six Sigma: A Philosophy
A vision of process performance
Tantamount to “zero defects”
A “Management Mantra”

## Slide 89: Six Sigma: A Method
Really a Collection of Methods:
  Product/Service Design
  Quality Control
  Quality Improvement
  Strategic Planning

## Slide 90: Where Does “3.4 PPM” Come From?
Six Sigma is commonly defined to be equivalent to 3.4 defective parts per million.
Juran says that a Six Sigma process will produce only 0.002 defective parts per million.
What gives?

## Slide 91: Normal Curve Probabilities

## Slide 93: Process Centered between Spec Limits

## Slide 94: Process Shifted by 1.5 Standard Deviations

## Slide 95: Where Does “3.4 PPM” Come From?
The 3.4 defective parts per million definition of Six Sigma includes a “worst case” scenario of a 1.5 standard deviation shift in the process.
It is assumed that there is a very high probability that such a shift would be detected by SPC methods (low probability of Type II error).

## Slide 96: Six Sigma in Context
Is Six Sigma dramatically different from old-fashioned quality control?
Is Six Sigma a departure from 1980’s-style TQM?

## Slide 97: Six Sigma in Context
What Is New?
  Focus on Quantitative Methods
  Focus On Control
  A Higher Standard
  A New Metric for Defects (PPM)
  Lots of training
  Linkage between quality goals and employee incentives?

## Slide 98: Using Six Sigma
A New Standard; Not Adopted Uniformly across Industries
Beyond Generalities, Need to Develop Organization-Specific Methods
Hard Work, Not Magic
“A Direction Not a Place”

## Slide 99: Summary
Quality and Six Sigma: Basic ideas and history
Juran Trilogy
  Control
  Improvement
  Planning
Quality Strategy
Focus on Statistical Methods
  Process Capability ideas and metrics
  Control charts for attributes and variables